## Slide 1
S U D A R S H A N · S P P N S P A C E R E S E A R C H T E A M
ASTRA-MINE
Autonomous AI-Driven Extraterrestrial Resource Prospecting & ISRU Demonstrator
“Mine the resource. Optimize the mission. Build the future.”
AI
ROBOTICS
EMBEDDED SYSTEMS
SPACE TECHNOLOGY
RESEARCH
Mini-Project Presentation · 2026
github.com/Shreyasderaje/ASTRA-MINE

## Slide 2
WHAT WE SET OUT TO DO
Objectives
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
02
01
Build an autonomous rover
4-wheel prototype with AI 'brain' (Raspberry Pi 5) and real-time 'reflexes' (ESP32) on a 3 m lunar-analogue testbed
02
Map buried resources with AI
Camera-proxy perception fused into a live resource-probability map of unknown terrain
03
Decide where to mine
Resource-energy-risk target selection - the rover computes the best site per unit of energy
04
Close the autonomous loop
Survey → decide → navigate → mine → return → deliver, with self re-planning
05
Benchmark the decision making
Four strategies compared on identical terrain: resource yield per watt-hour (g/Wh)
06
Command it like a mission
Live Mission Control digital twin streaming pose, battery, decisions and yields

## Slide 3
WHY THIS PROJECT EXISTS
The Purpose
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
03
Every kilogram launched from Earth costs thousands of dollars — and a lunar base needs water, oxygen and building material forever.
THE EARTH-SUPPLY PROBLEM
✕
Launch everything from Earth
✕
Pay per kilogram, every mission
✕
No resupply independence
✕
Not scalable for a lunar economy
In-Situ Resource Utilization (ISRU) is NASA & ESA's active answer — use what is already there.
THE ISRU CHAIN — WHAT ASTRA-MINE DEMONSTRATES
✓
Find the resource (prospecting)
✓
Decide if it is worth the trip
✓
Extract and carry it
✓
Process → estimate usable yield
Water near the lunar poles can even become rocket propellant — energy in space buys more missions.
Our purpose: build and measure the decision intelligence such a mining system would need — at student scale, with real hardware.

## Slide 4
WHERE THIS TECHNOLOGY LANDS
Uses & Applications
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
04
1
Planetary & surface robotics
Lunar/Mars prospecting rovers; the same loop flies on future ISRU missions
2
Autonomous mining
Self-directed haul & dig decisions that optimize yield per litre of fuel
3
Disaster response
Robots that map rubble, find victims' zones and ration battery autonomy
4
Unknown-terrain exploration
Caves, tunnels, poles, ocean floors — anywhere GPS and maps do not exist
5
Hazardous-site inspection
Nuclear, chemical and deep-industrial sites where humans should not walk
6
Precision agriculture
Soil-sensing scouts that decide where sampling pays off per unit energy
One architecture — sense → believe → decide → act — transfers to every one of these domains.

## Slide 5
HONEST ENGINEERING
Limitations & Environmental Impact
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
05
HONEST LIMITATIONS
Terrestrial analogue
we demonstrate the intelligence on proxy markers — not real lunar ice
Proxy sensing
colour-marked simulant stands in for spectral detection (future work: NIR)
Odometry-only localization
encoders + IMU drift a few %; no SLAM yet
Small, self-made dataset
vision model is trained on our own synthetic + testbed data
Prototype-scale energy model
calibrated to ≈15% on the testbed, not flight-grade
ENVIRONMENTAL RESPONSIBILITY
No real chemistry
water → propellant is a modelled pathway; we never produce or store H₂/O₂
No planetary contamination
everything happens in an indoor sand testbed — the Moon stays untouched
Reusable standard parts
COTS electronics chosen for re-use across semesters → minimal e-waste
Battery stewardship
sealed Li-ion pack with BMS; retired cells routed to e-waste recycling
Tiny energy footprint
≈40 Wh per mission — less than a laptop hour
We say these out loud — scope honesty is part of the engineering.

## Slide 6
THE BRAIN — IDENTICAL IN SIMULATION & ON THE ROVER
Software Architecture
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
06
CAMERA + TOF
sensing
PERCEPTION
OpenCV proxy
BELIEF MAP
probability
MISSION OPTIMIZER
score sites
A* PLANNER
energy + risk
MISSION FSM
state machine
◀ closed loop: every delivery re-scores every remaining target ◀
HARDWARE ABSTRACTION LAYER (HAL)
One interface, two worlds: SIMULATOR (physics + noisy sensors)
and REAL ROVER (ESP32 over serial) — zero brain changes.
MISSION CONTROL — DIGITAL TWIN
FastAPI + WebSocket dashboard: live map, pose, battery,
AI decisions, energy and yield — in the browser.
Python
OpenCV
NumPy
FastAPI
21 automated tests
100% run in CI-style suite
GitHub: Shreyasderaje/ASTRA-MINE — full source, docs and experiments.

## Slide 7
MISSION CONTROL, LIVE
The Digital Twin — See It Working
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
07
Live telemetry, 2× / second
pose, heading, battery, energy, AI decision, planned path, yield
Map starts unknown
rocks appear as the ToF finds them; resource zones from camera + operator cues
Same code, two worlds
SIMULATION mode today — REAL ROVER mode drives the physical rover
Measured, not claimed
energy integrated by the INA219 chip; grams weighed by the station load cell
Live run shown: 241 g delivered · 200 g/Wh · 0 collisions

## Slide 8
WHAT WE PHYSICALLY BUILD
Hardware Architecture
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
08
RASPBERRY PI 5 — “BRAIN”
AI vision · planning · mission logic · digital twin server · Wi-Fi dashboard
USB
ESP32 — “REFLEXES” (50 Hz)
real-time motor loop, odometry, gyro fusion, failsafes — things Linux cannot do
ONBOARD SENSORS & ACTUATORS
TB6612 → 4× DC motors
wheel encoders
MPU-6050 IMU
INA219 power
VL53L0X ToF
scoop servo
POWER
3S Li-ion 11.1 V (40 Wh) + BMS · inline fuse · buck converter 5 V rail · common ground bus
PROCESSING STATION — 2nd ESP32 + HX711 load cell
Weighs every delivery and streams the measured grams — the honest number behind g/Wh. Failsafes: 600 ms command watchdog · tilt cut-off · manual override.
Max speed
0.12 m/s
Battery
40 Wh
Sensors
6 onboard + camera
Testbed
3 m × 3 m
Budget
₹35k–50k
Team
4 × 16 weeks

## Slide 9
OUR RESEARCH CONTRIBUTION
The Rover Doesn't Follow a Path — It Decides
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
09
Mission Score = P(resource) × expected yield
÷ ( E_travel + E_mine + E_return ) × ( 1 + w·risk )
Every reachable target re-scored after each delivery — a closed-loop autonomous prospector.
NEAREST
always the closest zone
BASELINE
SHORTEST PATH
cheapest route wins
BASELINE
RESOURCE-GREEDY
richest zone, cost ignored
BASELINE
FULL (OURS)
value ÷ energy ÷ risk — all three traded off
OUR CONTRIBUTION
Why it matters: a rover that spends 1 Wh to fetch 1 g is useless — the optimizer maximizes grams per watt-hour, the currency of deep-space robotics.

## Slide 10
15 TERRAINS × 4 STRATEGIES · IDENTICAL ENERGY BUDGET
Results: Decisions Beat Default
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
10
Chart: 
| nearest | shortest path | resource greedy | FULL (ours)
g per Wh | 300.8 | 302.9 | 345.6 | 337.2
WHAT THE DATA SAYS
+14.9%
resource yield per watt-hour vs the nearest-target baseline (best strategy)
+12.1%
our full optimizer vs baseline — same mission, 9% less energy and 14% less travel than resource-greedy
Honest note: at 3 m scale travel is cheap, so resource-greedy ties. The scale study (3 m → 5 m) tests where the optimizer's edge grows.
Source: our own experiment — software/results/experiments.csv, 15 seeded terrains, 1.2 Wh budget, 0 collisions across 60 runs.

## Slide 11
OUR PIECE OF THE MOON
Lunar Analogue Testbed & ISRU Pathway
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
11
3 m × 3 m TESTBED — TOP VIEW
STATION
rocks ○ resource zones ○○ rover ▲ station ■
Craters, slopes and rocks are rebuilt to match the simulator — the sim is a 1:1 model of this floor.
1
SCOOP
rover collects marked simulant
2
DELIVER
returns to the processing station
3
WEIGH
load cell measures the true grams
4
YIELD MODEL
recoverable fraction → resource estimate
5
PROPELLANT MODEL
electrolysis → theoretical H₂ + O₂ (modelled only)
Demonstrates the full ISRU chain — without ever producing a dangerous chemical.

## Slide 12
16 WEEKS, 4 MEMBERS
Execution Plan
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
12
WEEKS 1–4
DESIGN + SIMULATION
architecture · world simulator · vision dataset · strategy experiments
SOFTWARE: DONE
WEEKS 5–7
ROVER BUILD
chassis · power · firmware · bring-up checks B1–B10
build phase
WEEKS 8–9
PERCEPTION
camera on Pi · HSV/YOLO tuning · live detector
integration
WEEKS 10–12
AUTONOMY
calibration · ToF rocks · closed-loop missions on testbed
the real thing
WEEKS 13–16
PROVE IT
experiments · report · PPT · filmed demo day
delivery
Risk doctrine: manual override always wired · MVP first · modular mining mechanism · no hazardous chemistry · integration rehearsed weekly, not at the end.

## Slide 13
WHAT IT TAKES
Budget & Team Roles
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
13
BUDGET (REALISTIC, STUDENT-SCALE)
₹35k – ₹50k
recommended build · ₹20k–30k minimum viable
Mobility (chassis, motors, wheels, driver)
Power (3S pack, BMS, buck)
Brain (Pi 5 kit + camera)
Sensors (IMU, INA219, ToF, encoders)
Station node + scoop + testbed
No LiDAR, no lab-grade simulant — scope discipline is the budget strategy.
Shreyas Deraje
TEAM LEAD · AI & SYSTEM ARCHITECTURE
mission optimizer, perception, integration, research lead
Pruthviraj Anchan
ROBOTICS & MECHANISMS
chassis, drivetrain, scoop design, testbed construction
Puneeth
EMBEDDED & POWER
ESP32 firmware, wiring, battery system, sensor bring-up
Naveen M
SOFTWARE & DIGITAL TWIN
dashboard, telemetry, data logging, experiments

## Slide 14
WHERE ASTRA-MINE GOES NEXT
Future Scope
ASTRA-MINE · SUDARSHAN — SPPN Space Research Team
14
01
Multi-rover cooperative mining
rover teams that split prospecting, mapping and hauling — the direction NASA's CADRE mission is flying
02
Reinforcement learning on the twin
the simulator is a safe gym: train smarter target policies, deploy the winner on the rover
03
Spectral proxy sensing
near-infrared reflectance instead of colour markers — a step toward real volatiles detection
04
SLAM + field trials
replace odometry drift with proper mapping; take the rover outdoors on rough terrain
05
Open dataset release
publish the ASTRA-MINE Lunar Analogue Dataset for other student teams to benchmark on
The architecture is the product — every upgrade plugs into the same closed loop.

## Slide 15
Thank You
ASTRA-MINE — Autonomous AI-Driven Extraterrestrial Resource Prospecting & ISRU Demonstrator
Questions · live demo · github.com/Shreyasderaje/ASTRA-MINE
T E A M S U D A R S H A N · S P P N S P A C E R E S E A R C H T E A M
Shreyas Deraje
4VP24AI043
Pruthviraj Anchan
4VP24AI031
Puneeth
4VP25AI403
Naveen M
4VP25AI401